## Cheat sheet

FlightMode	Switch	Position
Position (Angle mode)
Altitude (GNSS support off)
Stabilized (Manual)
Rattitude
Acro
Mission
RTH

Power on/off
Power on: Hold power button on drone for 8sec until LEDs are on. The Speed Slider must be set to “Rabbit”! / Power off: Remove battery

Motor Start / Stop
Hold throttle stick in the lower right corner

Flying
Check location (rules and regulations) / Free space for GPS signals, no potential reflectors to avoid multi-path reception / Drone battery full, ST16 battery full / Check battery voltage during flight

Bind mode: nsh shell command "typhoon_bind start"